## Slide 1: Introduction
This document helps to understand the SW architecture. It’s not complete, nor exhaustive, but should allow anyone to navigate into the source tree with ease.

## Slide 2
RSP : Robot support package
BSP : Board support package
FreeRtos
Drivers
External Library
ArduinoCore
ArdOs
Actuators
Log
Code ARD
AL : Applicative Layer
Strategies
ActuatorsCtrl
Nav
Detection
Core
ComStack
FSM
Yakindu
Legend:
Robot2017
HMI
CMSIS
BSP init X
Sensors
RobotX : Executable for Robot x
UT_X : Unit Test x
main
main
RemoteControl
BSP init
BSP init
Com : Board support package
Vizu (Python)
hdlc
Hdlc Py binding
com
core
gui
main
nanopb
protobuf
msg
C gen code
Py gen code

## Slide 3: Libraries
BSP : contains all HW related stuff (drivers), with no intelligence
Com : a shared package between communicating SW to handle the network layer
RSP : provides SW bricks to create a robot
AL : provide robot functionalities and workflows (how/when functionalities are activated)
RobotX (one for each robot) : assemble and configure robot specific items.
Vizu : the IT SW providing introspection on the robots

## Slide 4: Zoom on BSP
Component | Responsibility / description
CMSIS | Microcontroller low level drivers from Atmel (external lib) (see Yellow/Orange parts below).
FreeRtos | Operating system : provides a multiplexed environment so that several execution units may share the CPU (external lib).
ArduinoCore | Arduino framework (external lib with ARD updates).
Drivers | Drivers for peripherals (see green parts below)
BSP init | One file for each robot : instanciate and initiate drivers to fit the the robot specific HW distribution.
Board
uC
CPU
Timers
RAM
I2C
Stepper motor
(peripheral)
Pump transistor
Some examples to explain microcontroller/CPU/peripherals concepts :

## Slide 5: Zoom on COM
Component | Responsibility / description
hdlc | Make a byte stream  message stream conversion (framing). (external lib with ard updates)
Hdlc Py Binding | Cpython wrapper so that hdlc is accessible from python (external lib with ard updates)
Nanopb | A protobuf light compiler for embedded serialization (external lib)
protobuf | Protobuf module for Python (external module)
msg | .proto files describing communication message payloads
C gen code | C code generated from msg folder with nanopb
Py gen code | Python code generated from msg folder with protobuf
See next slide for a zoom on communication stack assembly

## Slide 6
Message level :
Byte level :
FreeRtos
Proto + generated code
ComOnUart.cpp
ArdHdlc.py
C/C++
Data/Function level :
ArdSerial.py
Python
Legend:
RemoteControl.py
ArdHdlc.cpp
ArdSerial
CMSIS
buffer_tools
RemoteControl.cpp
hdlc.c
python4ardHdlc.c
QSerialPort (QT)
CommonMsg.proto
Types.proto
RemoteControl.proto
The equivalent of ComOnUart is missing on python side for laziness. It’s included into RemoteControl.py

## Slide 7: Zoom on RSP
Component | Responsibility / description
ArdOS | A C++ decorator over FreeRtos
Core | Common helpers and mathematical tools
Nav/Detection | Moves/Localise robot and provide avoidance capability (will need further breaking in smaller parts)
HMI | Drives LEDs, buzzer and monitor key inputs
Sensors | Sensor driver decorators taking the mechanics into account (a TCS34725 driver provides rgb measures, a CylinderSensor provides a cylinder face)
Actuators | Actuators decorators taking the mechanics into account
Log | Log layer for Sdcard and network diffusion.
ComStack | Communication stack assembly (ex: pick Uart driver from BSP, hdlc from Com, …)
Zoom on AL
Component | Responsibility / description
ActuatorsCtrl | Actuators systems workflows. In general several actuators and sensors are working together to provide a robot feature
Strategies | Robot AI
Robot2017 | Assemble all robot bricks into a unique class to provide a class and deterministic initialization process.
RemoteControl | Provide a network interface to teleop the robot and to send telemetry messages to Vizu.

## Slide 8: Interrupts / Threading
Type | Function | Occurence | Content
IT | veryFast_interrupt | Period : 50 us | Stepper motor commands.
IT | fast_interrupt | Period : 1 ms | SW GPIO filters.
IT | ArdUART::IrqHandler | Every byte sent Every byte received | Read/Send UART data.
IT | Servo_Handler | Period : 1 ms | Servo commands.
IT | TwoWire::onService | I2C event | Read/Send I2C data.
IT | SysTick_Handler | Period : 1ms | Boot time count
Thread | prvIdleTask | When no other thread is running | “Empty”.
Thread | ComOnUart::Receiver::run | Episodic | Reads what ArdUART::IrqHandler has provided .
Thread | ComOnUart::Sender::run | Episodic | Feeds ArdUART::IrqHandler.
Thread | HmiThread::run | Period : 50 ms | LEDs commands.
Thread | StrategyThread::run | Episodic | Robot artificial intelligence
Thread | PollerThread::run | Period : 100 ms | Actuators/Sensors commands.
Thread | Navigation::run | Period : 20ms | Robot displacement management
The K_thread_config.h file contains all the threading/interrupt configuration.
The Robot2017.cpp file contains most of interrupts mapping.
Thread mapping is done in each SW component instanciated by the Robot2017 class.
Thread mapping should have been done in Robot2017.cpp to decouple threading and functions. It would also help to have a synthetic view of instanciated threads and prevent the need for K_thread_config.h